CiA Draft Work Draft Proposal 415

CANopen

Device Profile for Road Construction Machinery

This is a draft standard proposal and not suitable to be implemented

Version 0.2

Date: XX January 2003

© CAN in Automation (CiA) e. V.

HISTORY

| Date | Changes |
| --- | --- |
| XX.XX.2003 | First publication |

CONTENTS

1	Scope	6

2	Normative references	6

3	Acronyms and abbreviations	6

4	Definitions and operating principles	7

4.1	Introduction	7

4.2	Events	7

4.2.1	Introduction	7

4.2.2	Event description	7

5	Physical layer definitions	9

6	Error handling	9

6.1	Principle	9

6.2	Error behavior	9

6.3	Additional error code meanings	9

7	Predefinitions	10

7.1	General	10

7.2	Complex data types	10

7.2.1	Record 80h: Curvilinear	10

7.3	Predefined communication objects	10

7.3.1	Object 1000h: Device type	10

7.3.2	Object 1001h: Error register	10

7.3.3	Object 1029h: Error behavior	10

7.3.4	Object 67FFh: Device Type	11

7.4	PDO communication and mapping parameter	11

8	Object dictionary	12

8.1	Introduction and overview	12

8.2	6010h: Sensor functionality	13

8.3	6020h: Event	14

8.4	6100h: Position	15

8.5	6101h: Angle position	16

8.6	6102h: Curvilinear coordinates	17

8.7	6103h: Level deviation	19

8.8	6110h: Paver speed	20

8.9	6190h: Tow arm slope	21

8.10	6200h: Thickness	22

8.11	6210h: Evenness	23

8.12	6240h: Screed width	24

8.13	6250h: Volume	25

8.14	6300h: Material core temperature	26

8.15	6310h: Ambient temperature	27

8.16	6311h: Base temperature	29

8.17	6320h: Wind speed	29

8.18	6330h: Surface temperature	30

8.19	6410h: Required information	31

8.20	6500h: Position	32

8.21	6501h: Angle position	33

8.22	6502h: Curvilinear coordinates	34

8.23	6503h: Level deviation	36

8.24	6510h: Paver speed	37

8.25	6590h: Tow arm slope	37

8.26	6600h: Thickness	38

8.27	6610h: Evenness	40

8.28	6640h: Screed width	40

8.29	6650h: Volume	41

8.30	6700h: Material core temperature	42

8.31	6710h: Ambient temperature	44

8.32	6711h: Base temperature	45

8.33	6720h: Wind speed	45

8.34	6730h: Surface temperature	46

# Scope

The CANopen device profile for road construction machinery specifies the communication behavior of OSYRIS compliant modules. Devices compliant to this profile shall use communication techniques, which conform to those in the CiA Draft Standard 301. This specification should be consulted in parallel to this device profile specification.

This device profile has been jointly developed with the OSYRIS (Open System for Road Information Support) consortium (www.osyris.org) and the European Asphalt Pavement Association (EAPA).

# Normative references

/1/:	CiA DS 301 V4.02: CANopen application layer and communication profile, February 2002

/2/	CiA DSP 302 V3.2: Framework for programmable CANopen devices, January 2003

# Acronyms and abbreviations

CAN

Controller Area Network. Data link layer protocol for serial communication as specified in ISO 11898-1 (1999).

COB

Communication OBject, which is made of one or more CAN frames. Any information transmitted via CANopen has to be mapped into COBs.

COB-ID

COB-Identifier. Identifies a COB uniquely in a CAN network. The identifier determines the priority of that COB in the data link layer, too.

SDO

Service Data Object. Peer-to-peer communication with access to the Object Dictionary of a CANopen device.

OSYRIS

Open SYstem for Road Information Support. Product model for the road construction process.

RPDO

Receive Process Data Object. Communication object of a device, which contains output data.

SDO

Service Data Object. Peer-to-peer communication with access to the Object Dictionary of a CANopen device.

TPDO

Transmit Process Data Object. Communication object of a device, which contains input data.

# Definitions and operating principles

## Introduction

Devices compliant to this profile require an application master device with CANopen manager functionality capable to support self-configuration (Configuration manager) of the CANopen network. The CANopen manager shall scan the entire network during the start-up phase as defined by figure 1.

Fig. 1: CANopen boot-up procedure

The CANopen manager device shall start scanning the CANopen network for existing CANopen nodes by trying to access each node’s object dictionary entry 1000h using an SDO upload service. If the SDO upload fails, the corresponding node shall be ignored. After that, the functionality (number of supported objects) of each node at object 6010h sub-index 0h shall be read and the values shall be detected using a plausibility test, if any value seems illogically, the corresponding node shall be ignored. When receiving the valid number of entries, each sub-index entry shall be read out and a PDO-mapping for each node shall be created and written back to the corresponding node. At last the transmission type for each node shall be configured individually by the master according to the configuration of the system. The same procedure as with 6010h shall be repeated with 6410h. After running through this scanning process, the not ignored nodes shall be switched to Operational state by the NMT master. The application master shall send to each node by means of PDO write service a Data Status Request expecting ‘Data OK’ or ‘Data error’ (for further information see events, chapter 4.2).

## Events

### Introduction

By sending events the CANopen network is given the opportunity to exchange important system information of high priority. So defined events are always available for the CANopen manager device (in most application this will be the onboard computer), this is that the CANopen manager can manage measurements and appearing errors.

### Event description

Send Data Status

Server sends a data status request before starting the CAN network to receive information about connected/disconnected sensors (available/not-available data).

Data Status

Nodes answer with a data status report according data status request. This event could also appear during the operation of the machine, not only as an answer on a data status request.

Example: Message size for event ‘Wind speed‘ (object 6520h sub-index 0h), statement: ‘Sensor disconnected‘

| Byte 4 | Byte 3 | Byte 2 | Byte 1 |
| --- | --- | --- | --- |
| Sub-index: 0h | Index: 6520h | Code: 1h | Category: 1h |
| MSB |  |  | LSB |

General errors

No specific error is defined.

Start/Stop

State of the machine (movement, working status). Describes, if the machine stopped, is working or runs in the transfer mode (driving, but not working). The operator sends those events.

Leveling

Leveling status of the machine (manual, auto, and error). The operator sends manual and auto leveling mode, errors and ‘hydraulic output disabled‘ are sent.

Project

The operator decides about the beginning of a new project or a new mission, important for the initialization of the nodes (reset mode).

Note: The following list of events is common for compactor and paver.

| Event | Sub-index | Index | Code | Category | Explanation | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| Send Data Status | 00h | 0000h | 0h | 0h | - | Data status request of measured values |
| Data Status | Sub index | Index | 0h | 1h | Data available | Data OK (e.g. sensor connected) |
|  | Sub index | Index | 1h | 1h | Data not-available | Data error: sensor disconnected, other error |
|  | Sub index | Index | 2h | 1h | Data not-available | Data error: over-range |
|  | Sub index | Index | 3h | 1h | Data not-available | Data error: under-range |
| General errors | 00h | 0000 | 0h | 2h | - | reserved |
| Start/Stop | 00h | 0000h | 1h | 3h | Stop | Machine stops |
|  | 01h | 0000h | 1h | 3h | Work | Machine is moving and working |
|  | 02h | 0000h | 1h | 3h | Transfer | Machine is moving but not working |
| Leveling left | 00h | 0000h | 1h | 4h | Auto-Leveling off | Manual leveling |
|  | 01h | 0000h | 1h | 4h | Auto-Leveling on | Auto leveling |
|  | 00h | 0000h | 2h | 4h | Leveling error off | - |
|  | 01h | 0000h | 2h | 4h | Leveling error on | Error and hydraulic output is disabled |
| Leveling right | 00h | 0000h | 1h | 5h | Auto-Leveling off | Manual leveling |
|  | 01h | 0000h | 1h | 5h | Auto-Leveling on | Auto leveling |
|  | 00h | 0000h | 2h | 5h | Leveling error off | - |
|  | 01h | 0000h | 2h | 5h | Leveling error on | Error and hydraulic output is disabled |
| Project | 00h | 0000h | 1h | 6h | Start Project | Begin of project |
|  | 00h | 0000h | 2h | 6h | Start Mission | Begin of mission |

# Physical layer definitions

The definitions given in /2/ shall apply to devices compliant to this profile.

As a universal hardware interface between on-board computers and construction machinery the following connector is to be used, where the female connector is to be fixed on the machine, and the male connector is to be used by the on-board computer:

7-pin plug manufactured by ITT-Cannon (USA) "CA-02-COM-E16S-1S/P-B":

| A | E | L | M | N | P | S | T |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 27.4 | 24.6 | 24.7 | 14.2 | 3.2 | 22.4 | 32.5 | 3.2 |

[mm]

pin assignement:
A - Vcc+
B - CAN+
C - GND
D - CAN-

No additional specific physical layer definitions are specified.

# Error handling

## Principle

Emergency Messages shall be triggered by internal errors in the device and they are assigned the highest possible priority to ensure that they get access to the bus without latency. By default, the Emergency Messages shall contain the error field with pre-defined error numbers and additional information.

## Error behavior

If a severe device failure is detected the module shall enter by default autonomously the pre-operational state. If object 1029h is implemented, the device can be configured to enter alternatively the stopped state or remain in the current state in case of a device failure. Device failures shall include the following communication errors:

- Bus-off conditions of the CAN interface

- Life guarding event with the state ‘occurred’

- Heartbeat event with state ‘occurred’

Severe device errors also can be caused by device internal failures.

## Additional error code meanings

No additional error codes have been defined.

# Predefinitions

## General

For general definitions see /1/. It is recommended to implement functionality.

## Complex data types

### Record 80h: Curvilinear

| Index | Sub-Index | Description | Data Type |
| --- | --- | --- | --- |
| 80h | 0h | Number of entries | Unsigned8 |
|  | 1h | Distance traveled low | Unsigned32 |
|  | 2h | Distance traveled high | Unsigned16 |
|  | 3h | Abscissa | Unsigned32 |
|  | 4h | Ordinate | Unsigned32 |

## Predefined communication objects

### Object 1000h: Device type

The object at index 1000h describes the type of device and its functionality. For multiple device modules the Additional information parameter shall contain FFFFh. In this case, the object 67FFh shall be implemented.

VALUE DEFINITION

| 31 | 24 | 23 | 16 | 15 | 0 |
| --- | --- | --- | --- | --- | --- |
| Machine type | Device profile number |
| Additional information | General information |
| MSB | LSB |

General information:

Device profile number:	415d

Additional information:

Machine type:

1: Paver
2: Compactor
3: Grader
4: Dozer
5: Milling Machine
6: Heater
7: Truck

### Object 1001h: Error register

The device-specific bit in the error register object is reserved.

### Object 1029h: Error behavior

This object specifies to which state the device shall be set, when a communication error or a device-internal error is detected.

VALUE DEFINITION

0 = pre-operational (only if current state is operational)

1 = no state change

2 = stopped

OBJECT DESCRIPTION

| INDEX | 1029h |
| --- | --- |
| Name | error_behavior |
| Object Code | Array |
| Data Type | Unsigned8 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_error_classes |
| Access | ro |
| Entry Category | Mandatory |
| PDO Mapping | No |
| Value Range | 1h to 2h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | communication_error |
| Access | rw |
| Entry Category | Mandatory |
| PDO Mapping | No |
| Value Range | 0h to 2h |
| Default Value | 1h |

| Sub-Index | 2h |
| --- | --- |
| Description | internal_device_error |
| Access | rw |
| Entry Category | Mandatory |
| PDO Mapping | No |
| Value Range | 0h to 2h |
| Default Value | 1h |

### Object 67FFh: Device Type

This objects shall describe the first virtual device in a multiple device module according to /2/.

## PDO communication and mapping parameter

There are no default PDOs defined at all. The TPDOs and RPDOs are generated dynamically during the boot-up procedure as described above.

# Object dictionary

## Introduction and overview

Each device compliant with this device profile shall share the CANopen Object Dictionary entries from index 6000h to 67FFh, where the measurements available from each node are listed in the area 6000h to 63FFh and the values needed by each node are specified in the area 6400h to 67FFh. The entries 6000h (type of machine), 6010h (sensor functionality) and 6410h (required information) are mandatory, every other entry is optional. The device implements only those objects that are relevant to the functionality of the node. Object Description and Entry Description are specified in /1/.

General sensor objects:

- Object 6010h: Sensor functionality

- Object 6020h: Event

Objects providing position and speed measurements:

- Object 6100h: Position

- Object 6101h: Angle position

- Object 6102h: Curvilinear coordinates

- Object 6103h: Level deviation

- Object 6110h: Paver speed

- Object 6190h: Tow arm slope

Objects providing geometrical measurements:

- Object 6200h: Thickness

- Object 6210h: Evenness

- Object 6240h: Screed width

- Object 6250h: Volume

Objects providing geometrical measurements:

- Object 6300h: Material core temperature

- Object 6310h: Ambient temperature

- Object 6311h: Base temperature

- Object 6320h: Wind speed

- Object 6330h: Surface temperature

Objects providing special measurements:

- Object 6340h: Pre compaction value

- Object 6341h: Vibration frequency

- Object 6342h: Tamper frequency

General receive object:

- Object 6410h: Required information

Objects receiving position and speed measurements:

- Object 6500h: Position

- Object 6501h: Angle position

- Object 6502h: Curvilinear coordinates

- Object 6503h: Level deviation

- Object 6510h: Paver speed

- Object 6590h: Tow arm slope

Objects receiving geometrical measurements:

- Object 6600h: Thickness

- Object 6610h: Evenness

- Object 6640h: Screed width

- Object 6650h: Volume

Objects receiving geometrical measurements:

- Object 6700h: Material core temperature

- Object 6710h: Ambient temperature

- Object 6711h: Base temperature

- Object 6720h: Wind speed

- Object 6730h: Surface temperature

Objects receiving special measurements:

- Object 6740h: Pre compaction value

- Object 6741h: Vibration frequency

- Object 6742h: Tamper frequency

## 6010h: Sensor functionality

This object shall provide the description of the sensor functionality (which sensors are implemented) by means of a supported object list (all objects in the range of 6100h to 63FFh).

VALUE DEFINITION

Sub-index 1h to 254h:

| 31 |  |  | 16 | 15 | 8 | 7 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Index | Sub-index | Length |
| MSB |  |  |  |  |  |  | LSB |

OBJECT DESCRIPTION

| INDEX | 6010h |
| --- | --- |
| Name | sensor_functionality |
| Object Code | ARRAY |
| Data Type | Unsigned32 |
| Category | Mandatory |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_supported_objects |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | 1_st_object |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | See value definition |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | 2_nd_object |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | No |
| Value Range | See value definition |
| Default Value | No |

to

| Sub-Index | FEh |
| --- | --- |
| Description | 254_th_object |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | No |
| Value Range | Value definition |
| Default Value | No |

Example 1: Speed sensor; it measures only the speed of the paver.

| Index | Sub-Index | Content |
| --- | --- | --- |
| 6010h | 0h | 01h |
|  | 1h | 6110 00 10h |

Example 2: Combined environmental sensor; it measures ambient temperature and wind.

| Index | Sub-Index | Content |
| --- | --- | --- |
| 6010h | 0h | 04h |
|  | 1h | 6520 00 10h |
|  | 2h | 6510 01 10h |
|  | 3h | 6510 02 10h |
|  | 4h | 6510 03 10h |

## 6020h: Event

This object shall provide the event message.

VALUE DEFINITION

See chapter 4.2.2.

OBJECT DESCRIPTION

| INDEX | 6020h |
| --- | --- |
| Name | event |
| Object Code | VAR |
| Data Type | Unsigned32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | See value definition |
| Default Value | No |

## 6100h: Position

This object shall provide the 3-D absolute position by measuring the position in the four cardinal points and the geodesic height.

VALUE DEFINITION

Sub-index 1h: E

Positive values: east direction; negative values: west direction shall be given in 1 mm per bit. An invalid measurement shall be indicated by a value of FFFF FFFFh.

Sub-index 2h: N

Positive values: north direction; negative values: south direction shall be given in 1 mm per bit. An invalid measurement shall be indicated by a value of FFFF FFFFh.

Sub-index 3h: H

Geodesic height shall be given in 0.1 mm per bit. An invalid measurement shall be indicated by a value of FFFF FFFFh.

OBJECT DESCRIPTION

| INDEX | 6100h |
| --- | --- |
| Name | Position |
| Object Code | ARRAY |
| Data Type | Signed32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 3h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | E |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Possible |
| Value Range | 0131 2C00h to 8131 2C00h |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | N |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Possible |
| Value Range | 0131 2C00h to 8131 2C00h |
| Default Value | No |

| Sub-Index | 3h |
| --- | --- |
| Description | H |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Possible |
| Value Range | Signed32 |
| Default Value | No |

## 6101h: Angle position

This object shall provide slope measurement (long slope, cross slope) and heading.

VALUE DEFINITION

Sub-index 1h: Long slope

The value shall be given in 0.01% per bit (positive value: uphill; negative value: downhill). An invalid measurement shall be indicated by a value of FFFFh.

Sub-index 2h: Cross slope

The value shall be given in 0.01% per bit (negative value: clockwise rotation). An invalid measurement shall be indicated by a value of FFFFh.

Sub-index 3h: Heading

The value shall be given in 0.0055° per bit (0000h = north; 4000h = west; FFFEh = full rotation). An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6101h |
| --- | --- |
| Name | angle_position |
| Object Code | ARRAY |
| Data Type | Signed32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 3h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | long_slope |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed32 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | cross_slope |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed32 |
| Default Value | No |

| Sub-Index | 3h |
| --- | --- |
| Description | Heading |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | See value definition |
| Default Value | No |

## 6102h: Curvilinear coordinates

This object shall provide the curve measurement, containing traveled distance, abscissa (distance relative to stationing) and ordinate (distance from axis to the right) value. The onboard computer (application master) or CANopen manager may reset the measured values (e.g. distance traveled low) by means of SDO services.

VALUE DEFINITION

Sub-index 1h: Distance traveled low

The value shall describe the total distance traveled (project/mission-specific or global) and shall be given in 1 mm per bit. An invalid measurement shall be indicated by a value of FFFF FFFFh.

Sub-index 2h: Distance traveled high

The value is increased by 1 each 232 mm (4,294 km).
An invalid measurement shall be indicated by a value of FFFFh.

Sub-index 3h: Abscissa

The value shall provide the measured distance relative to stationing, count down when maneuvering backwards. It shall be given in 1 mm per bit. An invalid measurement shall be indicated by a value of FFFF FFFFh.

Sub-index 4h: Ordinate

The value shall provide the measured distance from the axis to the right. It shall be given in 1 mm per bit (positive value: right-hand curve; negative: left-hand curve). An invalid measurement shall be indicated by a value of FFFF FFFFh.

OBJECT DESCRIPTION

| INDEX | 6102h |
| --- | --- |
| Name | curvilinear_coordinates |
| Object Code | RECORD |
| Data Type | 80h (curvilinear) |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 4h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | distance_traveled_low |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | distance_traveled_high |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

| Sub-Index | 3h |
| --- | --- |
| Description | abscissa |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | No |

| Sub-Index | 4h |
| --- | --- |
| Description | ordinate |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | No |

## 6103h: Level deviation

This object shall provide the level measurement.

VALUE DEFINITION

Sub-index 1h and 2h:

The values shall be given in 0.1 mm per bit (positive value: level too high; negative value: level too low). An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6103h |
| --- | --- |
| Name | level_deviation |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 2h |
| Default Value | 2h |

| Sub-Index | 1h |
| --- | --- |
| Description | level_deviation_left |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | level_deviation_right |
| Entry Description | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6110h: Paver speed

This object shall provide the current speed of the paver.

VALUE DEFINITION

The value shall be given in 1 mm/s per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6110h |
| --- | --- |
| Name | paver_speed |
| Object Code | VAR |
| Data Type | Unsigned16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

## 6190h: Tow arm slope

This object shall provide the slope measurement for the tow arm of the paver.

VALUE DEFINITION

Sub-index 1h and 2h:

The values shall be given in 0.01% per bit (positive value: tow arm up; negative value: tow arm down). An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6190h |
| --- | --- |
| Name | tow_arm_slope |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 2h |
| Default Value | 2h |

| Sub-Index | 1h |
| --- | --- |
| Description | towarm_slope_left |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | towarm_slope_right |
| Entry Description | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6200h: Thickness

This object shall provide thickness measurements of the laid layer. There are three mandatory measurements: average thickness over the entire width (sub-index 1h), thickness left side of the layer (sub-index 2h), and thickness left side of the layer (sub-index 3h). Additional thickness measurements may be supported in order to get a more precise profile of the laid layer.

VALUE DEFINITION

Sub-index 1h and FEh:

The values shall be given in 0.1 mm per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6200h |
| --- | --- |
| Name | thickness |
| Object Code | ARRAY |
| Data Type | Unsigned16 |
| Category | optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 3h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | thickness |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | thickness_left |
| Entry Description | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

| Sub-Index | 3h |
| --- | --- |
| Description | thickness_right |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

| Sub-Index | 4h |
| --- | --- |
| Description | thickness_1 |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

to

| Sub-Index | FEh |
| --- | --- |
| Description | thickness_251 |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

## 6210h: Evenness

This object shall provide the evenness measurement of the laid layer.

VALUE DEFINITION

The values shall be given in 1 mm/m per bit (positive value: uphill; negative value: downhill). An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6210h |
| --- | --- |
| Name | evenness |
| Object Code | VAR |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6240h: Screed width

This object shall provide the screed width measurements of the laid layer by measuring screed width extensions left and right as well as total screed width.

VALUE DEFINITION

Sub-index 1h to 3h:

The values shall be given in 0. 1 mm per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6240h |
| --- | --- |
| Name | screed_width |
| Object Code | ARRAY |
| Data Type | Unsigned16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 3h |
| Default Value | 3h |

| Sub-Index | 1h |
| --- | --- |
| Description | screed_width_left |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | screed_width_right |
| Entry Description | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

| Sub-Index | 3h |
| --- | --- |
| Description | total_screed_width |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

## 6250h: Volume

This object shall provide volume measurements since the beginning of the project (sub-index 1h) and beginning of the mission (sub-index 2h).

VALUE DEFINITION

Sub-index 1h and 2h:

The values shall be given in 0.001 m3 per bit. An invalid measurement shall be indicated by a value of FFFF FFFFh.

OBJECT DESCRIPTION

| INDEX | 6250h |
| --- | --- |
| Name | volume |
| Object Code | ARRAY |
| Data Type | Unsigned32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 2h |
| Default Value | 2h |

| Sub-Index | 1h |
| --- | --- |
| Description | total_volume |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | mission_volume |
| Entry Description | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | No |

## 6300h: Material core temperature

This object shall provide temperature measurements of the material.

VALUE DEFINITION

Sub-index 1h to 4h:

The values shall be given in 0.1 °C per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6300h |
| --- | --- |
| Name | material_core_temperature |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 4h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | temperature_average |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | temperature_left_side |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 3h |
| --- | --- |
| Description | temperature_right_side |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 4h |
| --- | --- |
| Description | temperature_center |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6310h: Ambient temperature

This object shall provide temperature measurements around the machinery including an average of all measured points (mandatory).

VALUE DEFINITION

Sub-index 1h to FEh:

The values shall be given in 0.1 °C per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6310h |
| --- | --- |
| Name | ambient_temperature |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | temperature_average |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | temperature_1 |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

to

| Sub-Index | FEh |
| --- | --- |
| Description | temperature_253 |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6311h: Base temperature

This object shall provide surface temperature measurements of the layer below the paver before laying of the new asphalt layer.

VALUE DEFINITION

The value shall be given in 0.1 °C per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6311h |
| --- | --- |
| Name | base_temperature |
| Object Code | VAR |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6320h: Wind speed

This object shall provide wind speed measurements around the machinery. It is required for the description and calculation of other measurements (e.g. temperature).

VALUE DEFINITION

The value shall be given in 0.01 m/s per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6320h |
| --- | --- |
| Name | wind_speed |
| Object Code | VAR |
| Data Type | Unsigned16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | No |

## 6330h: Surface temperature

This object shall provide surface temperature measurements of the new laid layer including an average of all measured points (mandatory).

VALUE DEFINITION

Sub-index 1h to FEh:

The values shall be given in 0.1 °C per bit. An invalid measurement shall be indicated by a value of FFFFh.

OBJECT DESCRIPTION

| INDEX | 6330h |
| --- | --- |
| Name | surface_temperature |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | temperature_average |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | temperature_1 |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

to

| Sub-Index | FEh |
| --- | --- |
| Description | temperature_253 |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | No |

## 6410h: Required information

This object shall indicate the description of the required sensor information to be received from other nodes by means of an object list (all objects in the range of 6500h to 67FFh).

VALUE DEFINITION

See object 6010h.

OBJECT DESCRIPTION

| INDEX | 6410h |
| --- | --- |
| Name | required_information |
| Object Code | ARRAY |
| Data Type | Unsigned32 |
| Category | Mandatory |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_supported_objects |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | 1_st_object |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | See value definition |
| Default Value | No |

| Sub-Index | 2h |
| --- | --- |
| Description | 2_nd_object |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | No |
| Value Range | See value definition |
| Default Value | No |

to

| Sub-Index | FEh |
| --- | --- |
| Description | 254_th_object |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | No |
| Value Range | Value definition |
| Default Value | No |

## 6500h: Position

This object shall receive the 3-D absolute position by measuring the position in the four cardinal points and the geodesic height.

VALUE DEFINITION

See object 6100h.

OBJECT DESCRIPTION

| INDEX | 6500h |
| --- | --- |
| Name | Position |
| Object Code | ARRAY |
| Data Type | Signed32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 3h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | E |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Possible |
| Value Range | 0131 2C00h to 8131 2C00h |
| Default Value | FFFF FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | N |
| Entry Description | Optional |
| Access | ro |
| PDO Mapping | Possible |
| Value Range | 0131 2C00h to 8131 2C00h |
| Default Value | FFFF FFFFh |

| Sub-Index | 3h |
| --- | --- |
| Description | H |
| Entry Category | Optional |
| Access | ro |
| PDO Mapping | Possible |
| Value Range | Signed32 |
| Default Value | FFFF FFFFh |

## 6501h: Angle position

This object shall receive slope measurement (long slope, cross slope) and heading.

VALUE DEFINITION

See object 6101h.

OBJECT DESCRIPTION

| INDEX | 6501h |
| --- | --- |
| Name | angle_position |
| Object Code | ARRAY |
| Data Type | Signed32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 3h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | long_slope |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed32 |
| Default Value | FFFF FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | cross_slope |
| Entry Description | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed32 |
| Default Value | FFFF FFFFh |

| Sub-Index | 3h |
| --- | --- |
| Description | Heading |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | See value definition |
| Default Value | FFFF FFFFh |

## 6502h: Curvilinear coordinates

This object shall receive the curve measurement, containing traveled distance, abscissa (distance relative to stationing) and ordinate (distance from axis to the right) value. The onboard computer (application master) or CANopen manager may reset the measured values (e.g. distance traveled low) by means of SDO services.

VALUE DEFINITION

See object 6102h.

OBJECT DESCRIPTION

| INDEX | 6502h |
| --- | --- |
| Name | curvilinear_coordinates |
| Object Code | RECORD |
| Data Type | 80h (curvilinear) |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 4h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | distance_traveled_low |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | FFFF FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | distance_traveled_high |
| Entry Description | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | FFFFh |

| Sub-Index | 3h |
| --- | --- |
| Description | abscissa |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | FFFF FFFFh |

| Sub-Index | 4h |
| --- | --- |
| Description | ordinate |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | FFFF FFFFh |

## 6503h: Level deviation

This object shall receive the level measurement.

VALUE DEFINITION

See object 6103h.

OBJECT DESCRIPTION

| INDEX | 6503h |
| --- | --- |
| Name | level_deviation |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 2h |
| Default Value | 2h |

| Sub-Index | 1h |
| --- | --- |
| Description | level_deviation_left |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | level_deviation_right |
| Entry Description | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6510h: Paver speed

This object shall receive the current speed of the paver.

VALUE DEFINITION

See object 6110h.

OBJECT DESCRIPTION

| INDEX | 6510h |
| --- | --- |
| Name | paver_speed |
| Object Code | VAR |
| Data Type | Unsigned16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | FFFFh |

## 6590h: Tow arm slope

This object shall receive the slope measurement for the tow arm of the paver.

VALUE DEFINITION

See object 6190h.

OBJECT DESCRIPTION

| INDEX | 6590h |
| --- | --- |
| Name | tow_arm_slope |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 2h |
| Default Value | 2h |

| Sub-Index | 1h |
| --- | --- |
| Description | towarm_slope_left |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | towarm_slope_right |
| Entry Description | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6600h: Thickness

This object shall receive thickness measurements of the laid layer. There are three mandatory measurements: average thickness over the entire width (sub-index 1h), thickness left side of the layer (sub-index 2h), and thickness left side of the layer (sub-index 3h). Additional thickness measurements may be supported in order to get a more precise profile of the laid layer.

VALUE DEFINITION

See object 6200h.

OBJECT DESCRIPTION

| INDEX | 6600h |
| --- | --- |
| Name | thickness |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 3h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | thickness |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | thickness_left |
| Entry Description | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 3h |
| --- | --- |
| Description | thickness_right |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 4h |
| --- | --- |
| Description | thickness_1 |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

to

| Sub-Index | FEh |
| --- | --- |
| Description | thickness_251 |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6610h: Evenness

This object shall receive the evenness measurement of the laid layer.

VALUE DEFINITION

See object 6210h.

OBJECT DESCRIPTION

| INDEX | 6610h |
| --- | --- |
| Name | evenness |
| Object Code | VAR |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6640h: Screed width

This object shall receive the screed width measurements of the laid layer by measuring screed width extensions left and right as well as total screed width.

VALUE DEFINITION

See object 6240h.

OBJECT DESCRIPTION

| INDEX | 6640h |
| --- | --- |
| Name | screed_width |
| Object Code | ARRAY |
| Data Type | Unsigned16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 3h |
| Default Value | 3h |

| Sub-Index | 1h |
| --- | --- |
| Description | screed_width_left |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | screed_width_right |
| Entry Description | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | FFFFh |

| Sub-Index | 3h |
| --- | --- |
| Description | total_screed_width |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | FFFFh |

## 6650h: Volume

This object shall receive volume measurements since the beginning of the project (sub-index 1h) and beginning of the mission (sub-index 2h).

VALUE DEFINITION

See object 6250h.

OBJECT DESCRIPTION

| INDEX | 6650h |
| --- | --- |
| Name | volume |
| Object Code | ARRAY |
| Data Type | Unsigned32 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 2h |
| Default Value | 2h |

| Sub-Index | 1h |
| --- | --- |
| Description | total_volume |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | FFFF FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | mission_volume |
| Entry Description | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned32 |
| Default Value | FFFF FFFFh |

## 6700h: Material core temperature

This object shall receive temperature measurements of the material.

VALUE DEFINITION

See object 6300h.

OBJECT DESCRIPTION

| INDEX | 6700h |
| --- | --- |
| Name | material_core_temperature |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to 4h |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | temperature_average |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | temperature_left_side |
| Entry Description | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 3h |
| --- | --- |
| Description | temperature_right_side |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 4h |
| --- | --- |
| Description | temperature_center |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6710h: Ambient temperature

This object shall receive temperature measurements around the machinery including an average of all measured points (mandatory).

VALUE DEFINITION

See object 6310h.

OBJECT DESCRIPTION

| INDEX | 6710h |
| --- | --- |
| Name | ambient_temperature |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | temperature_average |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | temperature_1 |
| Entry Description | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

to

| Sub-Index | FEh |
| --- | --- |
| Description | temperature_253 |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6711h: Base temperature

This object shall receive surface temperature measurements of the layer below the paver before laying of the new asphalt layer.

VALUE DEFINITION

See object 6311h.

OBJECT DESCRIPTION

| INDEX | 6711h |
| --- | --- |
| Name | base_temperature |
| Object Code | VAR |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

## 6720h: Wind speed

This object shall receive wind speed measurements around the machinery. It is required for the description and calculation of other measurements (e.g. temperature).

VALUE DEFINITION

See object 6320h.

OBJECT DESCRIPTION

| INDEX | 6720h |
| --- | --- |
| Name | wind_speed |
| Object Code | VAR |
| Data Type | Unsigned16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Unsigned16 |
| Default Value | FFFFh |

## 6730h: Surface temperature

This object shall receive surface temperature measurements of the new laid layer including an average of all measured points (mandatory).

VALUE DEFINITION

See object 6300h.

OBJECT DESCRIPTION

| INDEX | 6730h |
| --- | --- |
| Name | surface_temperature |
| Object Code | ARRAY |
| Data Type | Signed16 |
| Category | Optional |

ENTRY DESCRIPTION

| Sub-Index | 0h |
| --- | --- |
| Description | number_of_entries |
| Entry Category | Mandatory |
| Access | ro |
| PDO Mapping | No |
| Value Range | 1h to FEh |
| Default Value | No |

| Sub-Index | 1h |
| --- | --- |
| Description | temperature_average |
| Entry Category | Mandatory |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

| Sub-Index | 2h |
| --- | --- |
| Description | temperature_1 |
| Entry Description | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |

to

| Sub-Index | FEh |
| --- | --- |
| Description | temperature_253 |
| Entry Category | Optional |
| Access | rw |
| PDO Mapping | Optional |
| Value Range | Signed16 |
| Default Value | FFFFh |